LLYFNI VALE RAILWAY

TOKENS

No driver shall move his locomotive into a SECTION without being in possession of the appropriate TOKEN for that SECTION.

A STOP BOARD indicates the end of a SECTION and a locomotive may only proceed past a STOP BOARD, with caution, when a GREEN SIGNAL indicates that it is safe to do so.

It is the responsibility of the driver to ensure that the road ahead is safe for the locomotive to proceed.  If there is any doubt about the safety of the conditions the fireman should be sent ahead of the train on foot with a GREEN flag.  Having ascertained that that the road is clear and points are correctly set the locomotive may be called forward by raising the GREEN flag.

When leaving a SECTION the TOKEN for that SECTION must be handed to the STATION MASTER or placed in the TOKEN BOX, as appropriate, before departing the SECTION.

## EXCEPTIONS FOR SPECIAL CIRCUMSTANCES

When operating the full route with only one locomotive in steam a FULL LINE TOKEN may be issued providing that all other TOKENS are secured.  When operating with a FULL LINE TOKEN a STOP BOARD must be observed if a RED SIGNAL is showing but may be passed with caution when showing GREEN or with extreme caution if NO SIGNAL is showing.   In this circumstance particular attention should be given to the responsibility of the driver to ascertain the safety of the road ahead referred to above.

# By order of the Chief Engineer

Pontllyfni  1898